## Slide 1: CS385 Final Project
Michael Lang & Rachael Grabowski

## Slide 2: INSTRUCTION SET
Instruction | OP Code | Instruction | OP Code
add | 0000 | sw | 0110
sub | 0001 | slt | 0111
and | 0010 | beq | 1000
or | 0011 | bne | 1001
addi | 0100 | sll | 1010
lw | 0101 | srl | 1011

## Slide 3: Major Component Descriptions
Instruction Memory
  The instruction memory is represented by our input.hex file (see “input.hex” below)
ALU
  The ALU is a 16-bit ALU comprised of four 4-bit ALUs. It is capable of detecting overflow and zero.
Register File
  Register r0 is static 0 (it cannot change or be changed). The register file is 4-word by 16-bits-per-word.

## Slide 4: MAJOR COMPONENT DESCRIPTIONS
Control Unit
  The mainCtrl unit takes IFID_InstrMem[15:12] as input, and outputs a control signal to the IDEX register. The control options are: RegDst, BEQ, BNE, MemToReg, MemWrite, ALUsrc, RegWrite, SLL, SRL, and ALUctl.
input.hex
  The input.hex file is how we loaded our code into our program, instead of hard-coding our testing instructions. This made it very easy to swap between different sets of instructions for testing at various points in the project. MIPS ASM instructions were converted into binary, and those binary instructions were then converted into hex instructions. Those hex instructions were then read by the CPU module into instruction memory.